ENCOUNTER with INTER Molecular and BULK Susceptibility Effects in HRPMR studies SOLIDS; Proton Shielding Tensor Measurements

As stated above the HR PMR studies which are intended for determining Shielding tensor of protons are found to be beset by a difficulty; namely, every organic molecular system which is to be studied by HR PMR in single crystals had to be first of all made into spherically shaped specimens.

ENCOUNTER with INTER Molecular and BULK Susceptibility Effects in HRPMR studies SOLIDS; Proton Shielding Tensor Measurements

Not all the crystals grown have the characteristics to realize the spherically shaped specimen. This is so because making sphere out of the naturally grown morphology of the crystals required a sort of grinding that the crystals would not withstand and so the specimen might break into pieces even before nearing the spherical shape. Thus the applicability of the Multiple Pulse Line narrowing technique was limited only by the properly shaped specimen while from the point of view of NMR instrumentation the progress was proving to be a highly promising.

If there must be any necessity to study the improvement on the instrumentation part, it was necessary to find out whether there would really be so many numbers of samples to study. Instead of changing over, even from the point of view of basic research, the preoccupation was to find ways to circumvent the impediment and in simple terms the problem was to find out whether there is any way by which the intra molecular information on shielding can be retrieved from the experimentally determined Shielding tensor values from specimen of arbitrary shape.

Thus the basic approach had to be to sort out all the possible contributions to induced fields at a proton site in a single crystalline solid; and, find out how to disentangle them from the experimentally observed value.